## Slide 1: CSC141 - Introduction to Computer Programming Credit Hours 4(3,1)
Teacher:
AHMED MUMTAZ MUSTEHSAN

## Slide 2
Additional References:
1. Reference book:
“Programming Languages and Methodologies”
by Robert J. Schalkoff Publisher Jones and Barrlett
2. http://en.wikipedia.org/wiki/Flash_memory
3. www.slipperybrick.com

## Slide 3
RAM
Volatile Memory
ROM
Non-Volatile Memory
Loses its contents when power goes off
Doesn’t lose its contents when power goes off
Memory
Types of Memory

## Slide 4
Dynamic RAM (DRAM)
Used in Main Memory
Slower
Data needs to be refreshed periodically
Consumes more Power
Less Desirable
Cheap
Static RAM (SRAM)
Used in Cache Memory
Faster
Data DOES NOT need to be refreshed.
Consumes Less Power
More Desirable
Expensive
RAM
Types of RAM

## Slide 5
Memory Modules
SIMM
(Single Inline Memory Module)
72-pins
Transfers information over a 32-bit data path
DIMM
(Dual Inline Memory Module)
168 and 184-pins
Transfers information over a 64-bit data path
RIMM
(Robust ® Inline Memory Module)
184-pins
Transfers information over a 16-bit data path
Types of Memory Modules

## Slide 6: SIMM, DIMM and RIMM
Source:
Webanswers.com

## Slide 7: Cache Memory
The cache is a small amount of high-speed memory, usually with a memory cycle time comparable to the time required by the CPU to fetch one instruction.
The most frequently used instructions are kept in cache memory so that CPU can look there first. Saved time which was wasted by CPU in swapping instructions in and out of main memory.
It can be located on Microprocessor chip or on a separate chip next to CPU.

## Slide 8: Levels of Cache Memory
L1 (Primary or Internal Cache):
  Located directly on the processor chip
  Runs at the same speed as the CPU
  Small Capacity
L2 (Secondary or External Cache):
  Located directly on the processor chip
  Runs at CPU speeds (or nearly so)
  Larger capacity than L1 but slower than L1.
L3:
  Part of the system’s motherboard.
  Present in high-performance systems like servers.
  Larger capacity than L2 but slower than L2.

## Slide 9: Types of ROM
ROM (Read-Only Memory)
PROM (Programmable Read-Only Memory)
EPROM (Erasable Programmable Read-Only Memory)
EEPROM (Electrically Erasable PROM)
  Flash EEPROM

## Slide 10
ROM (Read-Only Memory)
  Also known as Firmware
  Manufactured with permanently written data.
  Cannot be erased or written on by the user.
PROM (Programmable Read-Only Memory)
  one-time programmable non-volatile memory
  manufactured blank
  depending on the technology, PROM can be programmed at final test.
EPROM (Erasable Programmable Read-Only Memory)
  Multiple times erasable programmable non-volatile memory
  It requires UV box to erase the EPROM

## Slide 11
EEPROM (Electrically Erasable PROM)
  user-modifiable read-only memory (ROM)
  can be erased and reprogrammed (written to) repeatedly through the application of higher than normal electrical voltage generated externally or internally
  For Example: Flash Memory.

## Slide 12: Flash Memory
Non-volatile Electrically Erasable Programmable Read-Only Memory
Examples: memory cards, USB flash drives, solid-state drives
Source: http://en.wikipedia.org/wiki/Flash_memory
www.slipperybrick.com

## Slide 13: CMOS Memory (BIOS Memory)
Small memory on PC motherboards that is used to store BIOS settings.
Traditionally called as CMOS RAM
It uses a low-power Complementary metal-oxide-semiconductor (CMOS) SRAM which is powered by a small battery to retain information when power goes off.
Stores configuration information about the computer
  Disk drives
  Keyboard
  Mouse‘
  Monitor
  Time/date.

## Slide 14: Processing
Input
Processing
Output
Input device
Central Processing Unit
Main Memory
Output Devices
Bus

## Slide 15
Data flow for a complete job
Input device
Central Processing Unit
Main Memory
Output Devices
Steps (b) and (c ) usually repeat many times
(a) First data flows from the input device into the main memory
Input device
Central Processing Unit
Main Memory
Output Devices
(c) Then CPU sends processed data back to main memory
Input device
Central Processing Unit
Main Memory
Output Devices
(d)Finally the results go to the output device
Input device
Central Processing Unit
Main Memory
Output Devices
(b) Next CPU brings the data into its registers for processing

## Slide 16
Programming Language

## Slide 17
Programming Language:
A programming Language is a notational system intended primarily to facilitate human-machine interaction.
The notational is understood both by human and machine.
The programming language has Syntax, and language elements have Semantics.

## Slide 18
What is a program?
A program is something that is produced using a programming Language.
A program is a structured entity with Semantics.

## Slide 19
What is programming?

## Slide 20
What is programming?
Programming is a Science:
  Because it implement the algorithms describe by mathematics and science.
Programming is a Skill:
Because it requires design efforts.
Programming is an Engineering:
Because it requires a tradeoffs between program size, speed, time (required for development and debugging) and maintainability among many solutions.
Programming is an Art
It requires creativity and employ imagination.

## Slide 21
Types of programming Languages

## Slide 22: Levels/Generations of Programming Languages
1st Generation Programming language (1GL)
  Machine Language: 0s or 1s
2nd Generation Programming language (2GL)
  Assembly Language : Mnemonics
3rd Generation Programming language (3GL)
  High-Level Languages ; (procedure oriented or Object Oriented)
4th Generation Programming language (4GL)
  Very-High-Level Languages
5th Generation Programming Language
  Natural Languages
CSC141 Introduction to Computer Programming

## Slide 23: Machine language (1GL)
The lowest level of language.
The language used to program the first-generation computers.
The instructions in 1GL are made of binary numbers, represented by 1s and 0s.
1s and 0s correspond to the on and off states of electrical switches.
Suitable for the understanding of the machine but very much difficult to interpret and learn by the human programmer.

## Slide 24: Assembly language (2GL)
Low-level language that allows a programmer to use abbreviations or easily remembered words instead of numbers.
These Observations are called Mnemonics. These Mnemonic are Opcode and Operands
For Example: ADD AX, BX
MOV CX, AX
INC CX
Op-code; ADD, MOV, INC
Operands AX, BX,CX

## Slide 25: Assembly language (2GL)
  Programmer can write instructions faster but it is still not an easy language to learn.
  Drawback: The language is specific to a particular processor family and environment. (Machine Dependent Language)
  Assembler – A program that translates the assembly language program into machine language.

## Slide 26: High Level languages (3GL)
A High-Level Language is an English-like language.
It is a refinement of a second-generation programming language.
It allowed users to write in familiar notation, rather than numbers or abbreviations.
Most High-level languages are not Machine Dependent.
Translator for High-level languages is either a Compiler or an Interpreter.
Examples of High-level languages:
  FORTRON
  COBOL
  BASIC
  C and C++

## Slide 27: Very-High-Level Languages (4GL)
4GLs are much more user-oriented and allow programmers to develop programs with fewer commands compared with 3GLs.
Non-Procedural Language; Programmers don’t have to specify all the programming logic, only tell the computer what they want done.
Saves a lot of time.
4GLs consist of report generators, query languages, application generators, and interactive database management system
For example:
  RPG III (Report Generator)
  SQL (Structured Query Language)
  NOMAD and FOCUS (DBMS)

## Slide 28: Natural Languages (5GL)
Two types
  Ordinary Human Languages; like English.
  Programming language that use human language to give people a more natural connection with computers.
5GLs are designed to make the computer solve a given problem without the programmer.
Natural languages are part of the field of study known as Artificial Intelligence.
  Develop machines to emulate human-like qualities such as learning, reasoning, communicating, seeing and hearing.

## Slide 29
Evolution of Programming

## Slide 30: Programming Paradigms
A number of programming paradigms are:
Procedural/Imperative Programming
Functional Programming
Declarative Programming
Object Oriented Programming
Event driven Programming
Parallel Programming

## Slide 31: Procedural or Imperative:
Imperative programs emphasize “tell what to do”
When we say “ Do this, then do this, then do this, and if xx, do this, otherwise do this” This is imperative programming:
They focus on evaluating expressions and storing results in a variable.
The most common imperative language consists of statements such as:
a = 10;
b = 5;
c = a + b;

## Slide 32: Procedural or Imperative: … Contd
Example of imperative languages are:
Assembly language
COBOL
Pascal
C and C++

## Slide 33: Is there any Best Programming Language?
Programming Language is probably used most efficient if it is well suited For a specific task.
For example
  Business applications are often written in COBOL.
  Beginners to programming use BASIC.
  Scientific programming is often undertaken with either FORTON, PASCAL or C.

## Slide 34: Language Evaluation Criteria
Readability: measure programmer ease in reading source code
Orthogonality: include context sensitive restrictions.
Applicability: this is best suited as “use the right tool for the job”
Writ ability: includes simplicity and orthogonality and support for the abstraction
Reliability: include type checking and inspection handling
Cost: includes learning and writing cost, productivity, compilation cost, execution cost, debugging cost etc.
Other: flexibility of control statements and availability of data structures

## Slide 35: History of C Language
A general-purpose computer programming language.
Developed between 1969 and 1973 by Dennis Ritchie at the Bell Telephone Laboratories for use with the UNIX operating system.
Descendant of Ken Thompson’s language “B”
The first C programming language standard was published in 1978 as “The C Programming Language” by Kernighan and Ritchie (K&R).
"ANSI C" was the second C programming language standard published in 1989.
ISO approved “ANSI C” in 1990.
The latest stable release is C11.