## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 15:
STACK Related Instructions

## Slide 2: Lecture 14: Review
Instruction Execution in Assembly
Assembly Language Examples:
Control Flow
  JMP Instruction
  LOOP Instruction
  LOOP Example
  Summing an Integer Array

## Slide 3: Lecture Outline
STACK Operations
  Runtime Stack
  PUSH Operation
  POP Operation
  PUSH and POP Instructions
  Using PUSH and POP
  Related Instructions

## Slide 4: Runtime Stack
Imagine a stack of Plates . . .
  Plates are only added/removed to/from the top
  LIFO (Last In First Out) structure
10
9
8
7
6
5
4
3
2
1
Top
Bottom

## Slide 5: Runtime Stack
Managed by the CPU, using two registers
  SS (stack segment)
  ESP (stack pointer) *
* SP in Real-address mode
00000006
00001000
00000FFC
00000FF8
00000FF4
00000FF0
Memory
Stack
ESP

## Slide 6: PUSH Operation (1 of 3)
A 32-bit push operation decrements the stack pointer by 4 and copies a value into the location pointed to by the stack pointer.
00000006
00001000
00000FFC
00000FF8
00000FF4
00000FF0
Memory
Stack
ESP
00000006
000000A5
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP
AFTER
BEFORE

## Slide 7: PUSH Operation (1 of 3)
A 32-bit push operation decrements the stack pointer by 4 and copies a value into the location pointed to by the stack pointer.
00000006
000000A5
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP
AFTER

## Slide 8: PUSH Operation (1 of 3)
A 32-bit push operation decrements the stack pointer by 4 and copies a value into the location pointed to by the stack pointer.
00000006
000000A5
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP
AFTER

## Slide 9: PUSH Operation (2 of 3)
Same stack after pushing one more integer:
00000006
000000A5
00000001
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP

## Slide 10: PUSH Operation (3 of 3)
Same stack after pushing one more integer:
The area in the direction ESP grows, is always available (unless the stack has overflowed).
00000006
000000A5
00000001
00000002
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP

## Slide 11: POP Operation
Copies value at stack[ESP] into a register or variable.
Adds n to ESP, where n is either 2 or 4.
  value of n depends on the attribute of the operand receiving the data
00000006
000000A5
00000001
00001000
00000FFC
00000FF8
00000FF4
00000FF0
ESP
AFTER
ESP
BEFORE
00000006
000000A5
00000001
00000002
00001000
00000FFC
00000FF8
00000FF4
00000FF0

## Slide 12: PUSH and POP Instructions
PUSH syntax:
  PUSH r/m16
  PUSH r/m32
  PUSH imm32
POP syntax:
  POP r/m16
  POP r/m32

## Slide 13: Using PUSH and POP
push esi ; push registers
push ecx
push ebx
mov esi,OFFSET dwordVal ; display some memory
mov ecx,LENGTHOF dwordVal
mov ebx,TYPE dwordVal
………
pop ebx ; restore registers
pop ecx
pop esi
Save and restore registers when they contain important values. PUSH and POP instructions occur in the opposite order.

## Slide 14: Example: Nested Loop
mov ecx,100 ; set outer loop count
L1: ; begin the outer loop
push ecx ; save outer loop count
mov ecx,20 ; set inner loop count
L2: ; begin the inner loop
;
;
loop L2 ; repeat the inner loop
pop ecx ; restore outer loop count
loop L1 ; repeat the outer loop
Remember the nested loop we created on page 129? It's easy to push the outer loop counter before entering the inner loop:

## Slide 15: Related Instructions
PUSHFD and POPFD
  push and pop the EFLAGS register
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
  PUSHA and POPA do the same for 16-bit registers

## Slide 16: Summary
STACK Operations
  Runtime Stack
  PUSH Operation:
    Decrement n bytes from ESP and store n bytes
  POP Operation:
    Read n bytes from location (ESP) and Increment n
  PUSH and POP Instructions
  Using PUSH and POP
  Related Instructions

## Slide 17: Reference
Most of the Slides are taken from Presentation:
Chapter 5
Assembly Language for Intel-Based Computers, 4th Edition
Kip R. Irvine
(c) Pearson Education, 2002. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.