## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 16: Procedures

## Slide 2: Lecture 15: Review
Elements are only added/removed to/from the top.
LIFO (Last In First Out) structure.
Managed by the CPU, using two registers:
  SS:ESP
PUSH and POP Instructions
PUSH syntax:
  PUSH r/m16
  PUSH r/m32
  PUSH imm32
POP syntax:
  POP r/m16
  POP r/m32
10
9
8
7
6
5
4
3
2
1
Top
Bottom

## Slide 3: Lecture 15: Review
(cont.)
PUSHFD and POPFD
  push and pop the EFLAGS register
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
  PUSHA and POPA do the same for 16-bit registers

## Slide 4: Lecture Outline
Defining and Using PROCEDURES
  Creating Procedures
  Documenting Procedures
  Example: SumOf Procedure
  CALL and RET Instructions
  Nested Procedure Calls
  Local and Global Labels
  Procedure Parameters
  Flowchart Symbols
  USES Operator

## Slide 5: Creating Procedures
Large problems can be divided into smaller tasks to make them more manageable.
A procedure is the Assembly equivalent of a Java or C++ function.
Following is an assembly language procedure named sample:
sample PROC
  .
  .
  .
  ret
sample ENDP

## Slide 6: Documenting Procedures
Suggested documentation for each procedure:
  A description of all tasks accomplished by the procedure.
  Receives: A list of input parameters; state their usage and requirements.
  Returns: A description of values returned by the procedure.
  Requires: Optional list of requirements called preconditions that must be satisfied before the procedure is called.

## Slide 7: Example: SumOf Procedure
;---------------------------------------------------------
SumOf PROC
;
; Calculates and returns the sum of three 32-bit integers.
; Receives: EAX, EBX, ECX, the three integers. May be
; signed or unsigned.
; Returns: EAX = sum, and the status flags (Carry,
; Overflow, etc.) are changed.
; Requires: nothing
;---------------------------------------------------------
  add eax,ebx
  add eax,ecx
  ret
SumOf ENDP

## Slide 8: CALL and RET Instructions
The CALL instruction calls a procedure
  pushes offset of next instruction on the stack
  copies the address of the called procedure into EIP
The RET instruction returns from a procedure
  pops top of stack into EIP

## Slide 9: CALL-RET Example (1 of 2)
main PROC
00000020 call MySub
00000025 mov eax,ebx
  .
  .
main ENDP
MySub PROC
00000040 mov eax,edx
.
  .
  ret
MySub ENDP
0000025 is the offset of the instruction immediately following the CALL instruction
00000040 is the offset of the first instruction inside MySub

## Slide 10: CALL-RET Example (2 of 2)
The CALL instruction pushes 00000025 onto the stack, and loads 00000040 into EIP
The RET instruction pops 00000025 from the stack into EIP
(stack shown before RET executes)

## Slide 11: Nested Procedure Calls
By the time Sub3 is called, the stack contains all three return addresses:

## Slide 12: Local and Global Labels
main PROC
jmp L2 ; error
L1:: ; global label
exit
main ENDP
sub2 PROC
L2: ; local label
jmp L1 ; ok
ret
sub2 ENDP
A local label is visible only to statements inside the same procedure. A global label is visible everywhere.

## Slide 13: Procedure Parameters (1 of 3)
A good procedure might be usable in many different programs
  but not if it refers to specific variable names
Parameters help to make procedures flexible because parameter values can change at runtime

## Slide 14: Procedure Parameters (2 of 3)
ArraySum PROC
  mov esi,0 ; array index
  mov eax,0 ; set the sum to zero
mov ecx,LENGTHOF myarray ; set number of elements
L1: add eax,myArray[esi] ; add each integer to sum
  add esi,4 ; point to next integer
  loop L1 ; repeat for array size
  mov theSum,eax ; store the sum
ret
ArraySum ENDP
The ArraySum procedure calculates the sum of an array. It makes two references to specific variable names:
What if you wanted to calculate the sum of two or three arrays within the same program?

## Slide 15: Procedure Parameters (3 of 3)
ArraySum PROC
; Receives: ESI points to an array of doublewords,
; ECX = number of array elements.
; Returns: EAX = sum
;-----------------------------------------------------
  mov eax,0 ; set the sum to zero
L1: add eax,[esi] ; add each integer to sum
  add esi,4 ; point to next integer
  loop L1 ; repeat for array size
ret
ArraySum ENDP
This version of ArraySum returns the sum of any doubleword array whose address is in ESI. The sum is returned in EAX:

## Slide 16: Flowchart for the ArraySum Procedure
Begin
push esi, ecx
eax = 0
add eax,[esi]
add esi,4
ecx = ecx - 1
ecx > 0?
pop ecx, esi
End
push esi
push ecx
mov eax,0
AS1:
add eax,[esi]
add esi,4
loop AS1
pop ecx
pop esi
Yes
No

## Slide 17: USES Operator
Lists the registers that will be preserved
ArraySum PROC USES esi ecx
mov eax,0 ; set the sum to zero
etc.
MASM generates the code shown in gold:
ArraySum PROC
push esi
push ecx
.
.
pop ecx
pop esi
ret
ArraySum ENDP

## Slide 18: When not to push a register
SumOf PROC ; sum of three integers
  push eax ; 1
  add eax,ebx ; 2
  add eax,ecx ; 3
  pop eax ; 4
  ret
SumOf ENDP
The sum of the three registers is stored in EAX on line (3), but the POP instruction replaces it with the starting value of EAX on line (4):

## Slide 19: Summary
Creating Procedures
Documenting Procedures
Example: SumOf Procedure
CALL and RET Instructions
The CALL instruction calls a procedure
  pushes offset of next instruction on the stack and copies the address of the called procedure into EIP
The RET instruction returns from a procedure
sample PROC
  .
  .
  .
  ret
sample ENDP

## Slide 20: Summary
Nested Procedure Calls
Local and Global Labels
Procedure Parameters
Flowchart Symbols
USES Operator
(cont.)

## Slide 21: Reference
Most of the Slides are taken from Presentation:
Chapter 5
Assembly Language for Intel-Based Computers, 4th Edition
Kip R. Irvine
(c) Pearson Education, 2002. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.