## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 17:
Boolean and Comparison Instructions

## Slide 2: Lecture 16: Review
Creating Procedures
Documenting Procedures
Example: SumOf Procedure
CALL and RET Instructions
The CALL instruction calls a procedure
  pushes offset of next instruction on the stack and copies the address of the called procedure into EIP
The RET instruction returns from a procedure

## Slide 3: Lecture 16: Review
(cont.)
Nested Procedure Calls
Local and Global Labels
Flowchart Symbols
USES Operator

## Slide 4: Lecture Outline
Boolean and Comparison Instructions
  CPU Status Flags
  AND Instruction
  OR Instruction
  XOR Instruction
  NOT Instruction
  Applications
  TEST Instruction
  CMP Instruction

## Slide 5: Status Flags - Review
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.

## Slide 6: Status Flags - Review
The Overflow flag is set when an instruction generates an invalid signed result (bit 7 carry is XORed with bit 6 Carry).
The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4

## Slide 7: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Syntax:
    AND destination, source
  (same operand types as MOV)
AND

## Slide 8: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Syntax:
    OR destination, source
OR

## Slide 9: XOR Instruction
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax:
    XOR destination, source
XOR
XOR is a useful way to toggle (invert) the bits in an operand.

## Slide 10: NOT Instruction
Performs a Boolean NOT operation on a single destination operand
Syntax:
    NOT destination
NOT

## Slide 11: Applications (1 of 4)
mov al,'a' ; AL = 01100001b
and al,11011111b ; AL = 01000001b
Task: Convert the character in AL to upper case.
    ‘a’ = ASCII 7 Bits : 1100001
    ‘A’ = ASCII 7 Bits : 1000001
Solution: Use the AND instruction to clear bit 5.

## Slide 12: Applications (2 of 4)
mov al,6 ; AL = 00000110b
or al,00110000b ; AL = 00110110b
Task: Convert a binary decimal byte into its equivalent ASCII decimal digit.
    0 : ASCII : 0011 0000
    1 : ASCII : 0011 0001
    …….
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 13: Applications (3 of 4)
mov ax,wordVal
and ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.
JZ (jump if Zero) is covered in Next Lecture.
Your turn: Write code that jumps to a label if an integer is negative.

## Slide 14: Applications (4 of 4)
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 15: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the Zero flag is affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
test al,00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
test al,00000011b
jz ValueNotFound

## Slide 16: CMP Instruction (1 of 3)
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax: CMP destination, source
Example: destination == source
mov al,5
cmp al,5 ; Zero flag set
Example: destination < source
mov al,4
cmp al,5 ; Carry flag set

## Slide 17: CMP Instruction (2 of 3)
Example: destination > source
mov al,6
cmp al,5 ; ZF = 0, CF = 0
(both the Zero and Carry flags are clear)

## Slide 18: CMP Instruction (3 of 3)
Example: destination > source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
The comparisons shown here are performed with signed integers.
Example: destination < source
mov al,-1
cmp al,5 ; Sign flag != Overflow flag

## Slide 19: Summary
Examples of PROC
CPU Status Flags
AND Instruction
  AND destination, source
OR Instruction
  OR destination, source
XOR Instruction
  XOR destination, source
NOT Instruction
  NOT destination

## Slide 20: Summary
Applications
TEST Instruction
  Performs a nondestructive AND operation between each pair of matching bits in two operands. ZERO Flag
CMP Instruction
  CMP destination, source
  Zero (Dest. Equal) and Carry (Dest. Less) Flags

## Slide 21: Reference
Most of the Slides are taken from Presentation:
Chapter 6
Assembly Language for Intel-Based Computers, 4th Edition
Kip R. Irvine
(c) Pearson Education, 2002. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.