## Slide 1: CSC 221 Computer Organization and Assembly Language
Lecture 21:
Conditional and Block Structures:
Assembly Programs

## Slide 2: Lecture 20: Review
BT (Bit Test) Instruction
Copies bit n from an operand into the Carry flag
Syntax: BT bitBase, n
  bitBase may be r/m16 or r/m32
  n may be r16, r32, or imm8

## Slide 3: Lecture 20: Review
LOOPZ (LOOPE)
Syntax:
  LOOPE/LOOPZ destination
Logic: ECX  ECX – 1 | if ECX > 0 and ZF=1, jump to destination
Useful when scanning an array for the first element that does not match a given value.
LOOPNZ (LOOPNE)
Syntax:
LOOPNZ/LOOPNE destination
Logic: ECX  ECX – 1; if ECX > 0 and ZF=0, jump to destination
Useful when scanning an array for the first element that matches a given value.
(cont.)

## Slide 4: Lecture 20: Review
Conditional Structures
Block-Structured IF Statements
Compound Expressions with AND
Compound Expressions with OR
WHILE Loops
REPEAT Loops
(cont.)

## Slide 5: Block-Structured IF Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 6: Compound Expression with AND
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:

## Slide 7: Compound Expression with OR (1 of 2)
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:

## Slide 8: WHILE Loops
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
top: cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 9: Using the .IF Directive
Runtime Expressions
Relational and Logical Operators
MASM-Generated Code
.REPEAT Directive
.WHILE Directive

## Slide 10: Runtime Expressions
.IF eax > ebx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF, .ELSE, .ELSEIF, and .ENDIF can be used to evaluate runtime expressions and create block-structured IF statements.
Examples:
MASM generates "hidden" code for you, consisting of code labels, CMP and conditional jump instructions.
.IF eax > ebx && eax > ecx
mov edx,1
.ELSE
mov edx,2
.ENDIF

## Slide 11: .REPEAT Directive
; Display integers 1 – 10:
mov eax,0
.REPEAT
inc eax
call WriteDec
call Crlf
.UNTIL eax == 10
Executes the loop body before testing the loop condition associated with the .UNTIL directive.
Example:

## Slide 12: .WHILE Directive
; Display integers 1 – 10:
mov eax,0
.WHILE eax < 10
inc eax
call WriteDec
call Crlf
.ENDW
Tests the loop condition before executing the loop body The .ENDW directive marks the end of the loop.
Example:

## Slide 13: LET’s ENJOY ASSEMBLY LANGUAGE

## Slide 14: Summary
ASSEMBLY IMPLEMENTATION OF:
Bit Test Instruction
  Copies bit n from an operand into the Carry flag
  Syntax: BT bitBase, n
Conditional LOOP Instructions
  LOOPZ and LOOPE
    LOOPZ/LOOPE destination
    Logic:
      ECX  ECX – 1
      if ECX > 0 and ZF=1, jump to destination
  LOOPNZ and LOOPNE
    LOOPZ/LOOPE destination
    Logic:
      ECX  ECX – 1
      if ECX > 0 and ZF=0, jump to destination

## Slide 15: Summary
ASSEMBLY IMPLEMENTATION OF:
Block Structures
  Block-Structured IF Statements
  Compound Expressions with AND
  Compound Expressions with OR
  WHILE Loops
  REPEAT Loops
(cont.)

## Slide 16: Reference
Most of the Slides are taken from Presentation:
Chapter 6
Assembly Language for Intel-Based Computers, 4th Edition
Kip R. Irvine
(c) Pearson Education, 2002. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.