## Slide 1: Computer Graphics
Lecture 03
Fasih ur Rehman

## Slide 2: Last Class
Introduction to Computer Graphics (Cont.)
  Visualization
  Image Processing
  Graphical User Interfaces (GUI)
Overview of Graphics Systems
  Display Devices

## Slide 3: Today’s Agenda
Overview of Graphics Systems
  Display Devices
    Colors and colored displays
    Raster displays and frame buffer

## Slide 4: CRT
Filament (acts as heating element, electrons emit from it in the form of beam)
Electrons move towards positive plate (Anode) focusing cylinder (Electric field)
Vertical and horizontal deflection plates have magnetic field in between them and control the position of the electron beam.
Beam strikes phosphor coating on front of tube producing illumination.
  Stronger the beam, brighter is the screen
  Longer the beam stays on a point brighter is the screen

## Slide 5: Characteristics of CRT
It’s massive evacuated glass tube
Capabilities of CRT are measured by
  Size of tube
  Brightness of the phosphors vs. darkness of the tube
  Speed of electron gun
  Diameter of the beam
  Pixels
Disadvantages are
  Size of the tube
  High power consumption
  Flicker
  Costly to refresh

## Slide 6: Characteristics of CRT (Phosphors)
Florescence is Light emitted while the phosphor is being struck by electrons
Phosphorescence is Light emitted once the electron beam is removed
  Persistence: The time from the removal of the excitation to the moment when phosphorescence has decayed to 10% of the initial light output

## Slide 7: Interlacing
http://escience.anu.edu.au/lecture/cg/Display/raster.en.html

## Slide 8: Video Formats
NTSC - 525x480, 30f/s, interlaced
PAL - 625x480, 25f/s, interlaced
VGA - 640x480, 60f/s, non-interlaced
SVGA – 800x600, 60f/s non-interlaced
RGB - 3 independent video signals and synchronization signal, vary in resolution and refresh rate
Time-multiplexed color - R,G,B one after another on a single signal, vary in resolution and refresh rate

## Slide 9: Colors
Additive Colors
  Red Green and Blue (sometimes White)
Subtractive Colors
  Yellow Cyan Magenta and Black
http://www.d.umn.edu/~mharvey/th1501color.html

## Slide 10: Color Display

## Slide 11: Raster Displays
Use sequential access
  Raster Displays (early 70s)
    like television, scan all pixels in regular pattern
    use frame buffer (video RAM) to eliminate sync problems
  RAM
    ¼ MB (256 KB) cost $2 million in 1971

## Slide 12: Frame Buffer
Raster images require frame buffers
Frame buffer - A block of memory, dedicated to graphics output, that holds the contents of what will be displayed.
If we want a frame buffer of 640 pixels by 480 pixels, we should allocate:
frame buffer = 640*480 bits
How many colors does 1 bit get you?
How many colors do 8 bits get you?
  Monochrome systems use this (green/gray scale)
What bit depth would you want for your frame buffer?

## Slide 13: Frame Buffer
No. of bytes in a frame buffer = 640*480*3
This way we can calculate memory of graphics card

## Slide 14: Summary
Overview of Graphics Systems
  Display Devices
    Colors and colored displays
    Raster displays and frame buffer

## Slide 15: References
Fundamentals of Computer Graphics Third Edition by Peter Shirley and Steve Marschner
Interactive Computer Graphics, A Top-down Approach with OpenGL (Third Edition) by Edward Angel.