## Slide 1: Computer Graphics
Lecture 05
Fasih ur Rehman

## Slide 2: Last Class
Overview of Graphic Systems
  Vector Displays
  Movie Standards
  LCD’s

## Slide 3: Today’s Agenda
Overview of Graphic Systems
  LED Display
  Plasma TV
  Hardcopy Devices
  Input Devices
Human Visual System
Ray Tracing

## Slide 4: LED Display
LED actually stands for Light Emitting Diode.
LED displays use the same technology for display but it uses LED’s for back light while LCD displays generally use Cold Cathode Fluorescent technology

## Slide 5: Comparison (Wikipedia)
Produce images with greater dynamic contrast
Can be extremely slim (some screens are less than 0.5 inch (0.92 cm) thin in edge-lit panels
Offer a wider color gamut (when RGB-LED backlighting is used)
Produce less environmental pollution on disposal
Are more expensive
Have longer lifespans and are more reliable
Have (typically) 20- to 30-percent lower power consumption
Run significantly cooler
Allow a wider dimming range
Are significantly lighter

## Slide 6: Plasma Panel
Plasma display panels
  Similar in principle to fluorescent light tubes
  Small gas-filled capsules are excited by electric field, emits UV light
  UV excites phosphor
  Phosphor relaxes, emits some other color

## Slide 7: Plasma Panel (Pros and cons)
Plasma panels are fairly bright and offer large viewing angle.
Good for Large format display
Plasma panels, however, are expansive, have large pixel size (~1mm as compared to ~0.2mm). Phosphor depletes with time and are less bright than CRT

## Slide 8: Hardcopy Devices
Inkjet Printer
Laser Printer
Film Recorder
Electrostatic Printer and
Pen Plotter

## Slide 9: Input Devices
Locator Devices:
  to indicate a position and/or orientation
  to select a displayed entity
  Tablet, Mouse, Trackball, Joystick, Touch Panel, Light Pen
Keyboard devices:
  to input a character string
  Alphanumeric keyboard (coded - get single ASCII character)
Valuator Devices:
  to input a single value in the space of real numbers
  Rotary dials (Bounded or Unbounded), Linear sliders
Choice Devices:
  to select from a set of possible actions or choices
  Function keys

## Slide 10: Human Visual System (HVS)

## Slide 11: Human Visual System (HVS)
Rods and cones are energized by electromagnetic energy in the range 350-780 nm
Sizes of rods and cones determines the resolution of HVS – our visual acuity
The sensors in the human eye do not react uniformly to the light energy at different wavelengths
Different HVS response for single frequency light – red/green/blue
Relative brightness response at different frequencies
The shown curve is known as Commision Internationale de L’Eclairage (CIE) standard
The curve matches the sensitivity of the monochromatic sensors used in black & white films and video camera
Most sensitive to GREEN colors

## Slide 12: Human Visual System (HVS)
HVS has three types of cones
  Blue
  Green
  Yellow

## Slide 13: Summary
Overview of Graphic Systems
  LED Display
  Plasma TV
  Hardcopy Devices
  Input Devices
Human Visual System

## Slide 14: References
Fundamentals of Computer Graphics Third Edition by Peter Shirley and Steve Marschner
Interactive Computer Graphics, A Top-down Approach with OpenGL (Third Edition) by Edward Angel.