## Slide 1: Module 2: Information Technology Infrastructure
Chapter 6: Telecommunications, Internet and Wireless Technology

## Slide 2: Learning Objectives
Identify the telecommunication media and hardware required for transmission
Identify the network types and key networking technologies (including protocols)
Discuss the principle technologies and standards for wireless networking
Describe several telecommunication applications that orgs benefit from today
Discuss how Internet works and its support for communications and e-business

## Slide 3: Intro to Telecommunications
Telecommunication
  Electronic transmission of signals for communication
  The general model of telecommunication consists of
    The sending device
    The medium
    The communication device
    The receiving unit

## Slide 4: Intro to telecommunications
Transmission medium
  Any material substance that carries an electronic signal to support communications between sending and receiving devices
  Divided into one or more communication channels
  Classified as simplex, half duplex, full duplex
  Characteristics:
    Bandwidth: rate at which data is exchanged (bps)
    Higher bandwidth, more channel transmits
    Broadband
    Latency: time it takes a signal to travel from one location to another
    Best combo: high bandwidth, low latency

## Slide 5: Intro to telecommunications
Physical transmission medium
Media Type | Description | Advantages | Disadvantages
Twisted pair cable | Twisted pair of copper wires, insulated | Used for telephone services, widely available | Transmission speed and distance limitation
Coaxial Cable | Inner conductor wire surrounded by insulation | Cleaner and faster data transfer than twisted pair | More expensive than twisted pair
Fiber-Optic cable | Extremely thin glass strands bound together in a sheathing, uses light to transmit | Less diameter, less distortion and high transmission rate | Expensive to purchase and install

## Slide 6: Intro to telecommunications
Wireless transmission medium
  Microwave
  Radio
  Infrared

## Slide 7: Intro to telecommunications
Telecommunication Hardware
  Modem
    Special device that converts digital signals to analog signals (modulation) and vice versa (demodulation)
    PC modem, cable modem, DSL modem
  Hub
    Device that connect network components, sending a packet of data to all other connected devices
  Switch
    Smarter than hub, forward data to specific destination
  Network Interface Card
    Network interface device, connection medium for linking network components

## Slide 8: Intro to telecommunications
Telecommunication Hardware
  Router
  WAP

## Slide 9: Computer Network
A network consists of two or more connected computers
A simple network contains:
  Client computer
  Dedicated server
  Network interfaces
  Connection medium
  Network operating system
  Hub/switch

## Slide 10: Computer Network

## Slide 11: Wired Network with Hub/Switch

## Slide 12: Two router Network

## Slide 13: Hybrid Network

## Slide 14: Computer Network
Types of Networks
  Local Area Networks (LAN): connects computer systems and devices within a small area, typically they are wired into office buildings
    Computers must be equipped with the correct interface
    Client/Server architecture: One computer is dedicated network file server, providing access to resources
    Ethernet: LAN standard for physical medium (10 Mbps)
    Fast Ethernet (100Mps), Gigabit Ethernet (1 Gbps)
    Peer-to-peer architecture: used in very small networks, different computers can exchange data by direct access and also peripheral devices. Useful for small businesses
  Metropolitan Area Networks (MAN): connects computers systems within a campus or a city
    Range of 30-90 miles

## Slide 15: Computer Network
Types of Networks
  Wide Area Networks (WAN):International Networks: connects large geographical regions
    Internet – world’s largest WAN
  Mesh Networking: way to route communications among network nodes by allowing for continuous connections and reconfiguration around blocked paths
    Robust, if one node fails, others can still communicate
    Can be used to provide Internet access, secure connections to corporate netowrks and VoIP calls

## Slide 16: Key Digital Networking Technologies
Client/Server computing
  Distributed computing model, some processing power on client computers
  Linked to network to server computers, sets rules for communication, provides every client with an address
Packet Switching
  Slicing digital messages into packets, sending them over communication paths, reassembling at destination
  Transmitted through routers

## Slide 17: Key Digital Networking Technologies
TCP/IP Connectivity
  Protocol: set of rules and procedures concerning transmission of information between 2 points in a network
  Now only worldwide standard Transmission Control Protocol/Internet Protocol (TCP/IP) is used with any kind of hardware for networking
  TCP: handles movement of data between computers, sequencing packets and acknowledging sending
  IP: delivery of packets and reassembling during transmission

## Slide 18: Wireless Communication
Advantages:
Helps businesses stay in touch with customers, suppliers, partners
Provides flexible arrangements for organizing work
Help create new products, services, sales channels
Provide easier access to remote corporate areas

## Slide 19: Wireless Communication Standards
Bluetooth
  Wireless N/W standard, creates PAN
  Range: 10m, 722Kbps (2.4Ghz)
  Useful for battery powered devices (printers, Keyboard)
  FedEx: signals transmitted from handheld devices through bluetooth
Wi-Fi (802.11)
  Standard for wireless LAN and wireless Internet access
  Range: 30-5-m, 11Mbps-54Mbps (2.4Ghz)
  Use: creating ‘hotspots’
  802.11 n is the fastest ( 100Mbps) based on the MIMO( multiple input/multiple output)

## Slide 20: Wireless Communication Standards
WiMAX
  Worldwide Interoperability for Microwave Access)
  Range: 31 miles, 75Mbps
  Use: areas where difficult to install broadband or Wi-Fi
  Connectivity provided by WiMAX towers

## Slide 21: Wireless Communication Standards
RFID
  Standard for radio signals to communicate with a tag
  Use: tracking movement of goods through supply chain
  RFID Tag
    embedded microchip and antenna
    Active: battery powered, send data automatically, expensive
    Passive: powered by the signals from reader, lighter, less expensive
  RFID Reader
    Reads tag, capturing the data, decodes it and send it over the network to the computer
    Reads data in its range
  Businesses need to update H/W and S/W to accommodate large data from RFID
  SAP, Oracle offer RFID-ready versions for SCM applications

## Slide 22: Cellular Network
ITU developed standard for cellular networks
  To standardize and allow global roaming
Mobile Communication standard
  Global System for Mobile Communication (GSM) and CDMA
  GPRS (General Packet Radio Service), EDGE, EVDO (Evolution Data Optimized)
  Earlier for voice and small data
  3G 144 Kbps to 2.4 Mbps
    Video, VoIP, graphics, rich media
  Next: 4G 100Mbps

## Slide 23: Telecommunication and Network Applications
Important Business applications include:
Linking Pcs to Mainframes/Servers
Voice Mail
  Send/receive store verbal messages
Small Business Networks
  Create small networks with few devices easily
  Either WAP with modem or a combo device (router, firewall, hub)
    Filtering and encryption
Electronic Document Distribution
  Send/receive digital documents
    Saves paper, access faster

## Slide 24: Telecommunication and Network Applications
Call Centres
Telecommuting/Virtual Workers
Videoconferencing
Electronic Data Interchange (EDI)
Electronic Funds Transfer (EFT)
Distance Learning
Team Collaboration

## Slide 25: Case Study: Delivering People More Efficiently Through Telecommunications
Crew Transportation Industry
  Shuttling crew members to train locations where they are needed
Problem:
  Slow to adopt telecomm technologies
  Van drivers could not communicate with dispatcher while in route
  Railway company not happy
RailCrewXpress
  Serving railways through technology platform
  Wireless telecommunication system that connects drivers with dispatchers and company IS
  Tracks drivers, dynamic routing change, maintains history of routes and driver times
  Data is analysed to optimize the efficiency of dispatches & routing

## Slide 26: Case Study: Delivering People More Efficiently Through Telecommunications
Challenges
  Economical networking technologies
  Automatically switch between satellite and GPRS data transmission
  Intelligently decide how much info to send and when
Next milestone
  RFID scanners to be installed in vans for tracking location

## Slide 27: Case Study: Delivering People More Efficiently Through Telecommunications
Advantages
  Faster and efficient communication between drivers and dispatchers
  Happier railway companies, because they get accurate ETAs
  Flexibility to accept new trip orders and reroute quickly
Real Time Monitoring
  Providing time-relevant info for quick decision-making
  View minute by minute info
  Respond quickly to changing conditions
  Analyse data for operational efficiency