## Slide 1: Previous Lecture 6
Resistors in Series
Current in a Series Circuit
Total Series Resistance
Application of Ohm's Law
Voltage Sources in Series
Kirchhoff's Voltage Law
Voltage Dividers

## Slide 2: Series Circuits
Power in Series Circuits
Voltage Measurements
Problems Solving
Lecture 7

## Slide 3: POWER IN SERIES CIRCUITS
The total amount of power in a series resistive circuit is equal to the sum of the powers in each resistor in series.
PT = P1 + P2 + P3 + ... + Pn
The following formulas are used to calculate the total power:

## Slide 4: Determine the total amount of power in the series circuit in the following Figure. (Solved on 2 slides)
RT=106Ω,PT= 2.12W ,IT= 142mA,P1= 200mW,P2= 360mW ,P3= 1.12 W ,P4= 441 mW

## Slide 5
RT=106Ω,PT= 2.12W ,IT= 142mA,P1= 200mW,P2= 360mW ,P3= 1.12 W ,P4= 441 mW

## Slide 6: Determine if the indicated power rating (1/2 W) of each resistor in the following circuit is sufficient to handle the actual power. If a rating is not adequate, specify the required minimum rating.
RT=7.91 kΩ,IT= 15mA,P1= 225mW ,P2= 608 mW ,P3= 205 mW ,P4= 743 mW

## Slide 7: VOLTAGE MEASUREMENTS
Voltage is relative. That is, the voltage at one point in a circuit is always measured relative to another point. This reference point in circuit is called the ground or common point.

## Slide 8: Determine the voltages with respect to ground of each of the indicated points in each circuit of following Figure. Assume that 25 V are dropped across each resistor.

## Slide 9: Some Important Formulas for Series Circuits

## Slide 10: Problems Solving
Resistors in Series
Current in a Series Circuit
Total Series Resistance
Application of Ohm's Law
Voltage Sources in Series
Kirchhoff's Voltage Law
Voltage Dividers
Power in Series Circuits
Voltage Measurements

## Slide 11: Problems related to Resistors in Series
Q.1 Connect each set of resistors in the following Figure in series between points A and B.
a) b)

## Slide 12: Problems related to Current in a Series Circuit
Q.1 What is the current through each resistor in a series circuit if the total voltage is 12 V and the total resistance is 120Ω?
100 mA

## Slide 13: Problems related to Total Series Resistance
Q.1 Calculate RT for each circuit of following Figure.
8.8 kΩ, 27.7 Ω, 17.84 MΩ

## Slide 14: Q.2 Six 56 Ω resistors, eight 100 Ω resistors, and two 22 Ω resistors are all connected in series What is the total resistance?
336 Ω + 800 Ω + 44 Ω = 1180 Ω

## Slide 15: Q.3 You have the following resistor values available to you in the lab in unlimited quantities: 1OΩ, 100 Ω, 470 Ω, 560 Ω, 680 Ω, 1.0 k Ω, 2.2 kΩ, and 5.6 kΩ. All of the other standard values are out of stock. A project that you are working on requires an 18 KΩ resistance. What combinations of the available values would you use in series to achieve this total resistance?
8(2.2 kΩ) + 4(100 Ω)= 18 kΩ or 3(5.6 kΩ) + 1 kΩ + 2(100 Ω) = 16.8 kΩ + 1 kΩ + 200 Ω = 18 kΩ

## Slide 16: Problems related to Application of Ohm's Law
Q.1 What is the current in the circuit of following Figure?
RT = 3.76 MΩ, 4.26 μA

## Slide 17: Q.2 Four equal-value resistors are in series with a 5 V battery, and 2.23 mA are measured. What is the value of each resistor?
RT=2.24 kΩ, Reach=560 Ω

## Slide 18: Q.3 What is the value of each resistor in the following circuit?
R1=330 Ω, R2=220 Ω, R2=100 Ω, R4=470 Ω

## Slide 19: Q.4 Determine VR1, R2 , and R3 in the following Figure.
V1=1.01 V, V2= 8.78V, R2= 714 Ω, R3=180 Ω

## Slide 20: Problems related to Voltage Sources in Series
Q.1 Series aiding is a term sometimes used to describe voltage sources of the same polarity in series. If a 5 V and a 9 V source are connected in this manner, what is the total voltage?

## Slide 21: Q.2 The term series opposing means that sources are in series with opposite polarities. If a 12 V and a 3 V battery are series opposing, what is the total voltage?

## Slide 22: Q.3 Determine the total source voltage in each circuit of the following Figure.
23 V, 35V, 0V

## Slide 23: Problems related to Kirchhoff's Voltage Law
Q.1 Five resistors are in series with a 20 V source. The voltage drops across four of the resistors are 1.5 V, 5.5 V, 3 V, and 6 V. How much voltage is dropped across the fifth resistor?
4 V

## Slide 24: Q.2 Determine the unspecified voltage drop(s) in the circuit of following Figure. Show how to connect a voltmeter to measure each unknown voltage drop.
6.8 V

## Slide 25: Q.3 Determine the unspecified voltage drop(s) in the circuit of following Figure. Show how to connect a voltmeter to measure each unknown voltage drop.
88 V

## Slide 26: Q.4 Find R1, R 2 , and R3 in the following circuit.
R1=560 Ω, R2= 220 Ω, RT=900 Ω, R3=120 Ω

## Slide 27: Q.5 In the circuit of following Figure, determine the resistance of R4
I=200 mA, R4=22 Ω

## Slide 28: Problems related to Voltage Dividers
Q. 1 The total resistance of a circuit is 560Ω. What percentage of the total voltage appears across a 27 Ω resistor that makes up part of the total series resistance?
4.82%

## Slide 29: Q.2 Determine the voltage with respect to ground for output A, B, and C in the following Figure.
RT=18.9KΩ, VA=15 V, VB= 10.6V, VC= 2.62V

## Slide 30: Q.3 What is the voltage across each resistor in the following Figure? R is the lowest-value resistor, and all others are multiples of that value as indicated.

## Slide 31: Problems related to Power in Series Circuits
Q.1 The following 1/4 W resistors are in series: 1.2kΩ, 2.2k Ω, 3.9k Ω, and 5.6k Ω. What is the maximum voltage that can be applied across the series resistors without exceeding a power rating? Which resistor will burn out first if excessive voltage is applied?
Imax=6.68 mA, V 1.2KΩ=8.02 V, V 2.2KΩ =14.7 V, V 3 .9KΩ = 26.1 V, V 5.6KΩ =37.4 V, VTmax=86.2 V
The 5.6 kΩ resistor is the limiting element in terms of power dissipation.

## Slide 32: Q.2 A certain series circuit consists of a 1/8 W resistor, a 1/4 W resistor and a 1/2 W resistor. The total resistance is 2400 Ω. If each of the resistors is operating in the circuit at its maximum power dissipation, determine the following: (Solved on 2 slides) (a) I (b) VT (c) The value of each resistor
I=19.1 mA, VT = 45.8 V, R1= 343 Ω,R2= 686 Ω,R3= 1.37 kΩ

## Slide 33
I=19.1 mA, VT = 45.8 V, R1= 343 Ω,R2= 686 Ω,R3= 1.37 kΩ

## Slide 34: Problems related to Voltage Measurements
Q.1 Determine the voltage at each point with respect to ground in the given circuit. (Solved on 2 slides)
RT=1.816 MΩ, VT=6V, IT= 3.3 μA, V1= 185 mV, V2=, 1.85 V V3=, 330 mV V4=, 3.3 V
VA= 14.82 V, VB= 12.97 V,VC=, 12.64 V ,VD= 9.34 V.

## Slide 35
RT=1.816 MΩ, VT=6V, IT= 3.3 μA, V1= 185 mV, V2=, 1.85 V V3=, 330 mV V4=, 3.3 V
VA= 14.82 V, VB= 12.97 V,VC=, 12.64 V ,VD= 9.34 V.

## Slide 36: Summary
Power in Series Circuits
Voltage Measurements
Problems Solving related to following topics
  Resistors in Series
  Current in a Series Circuit
  Total Series Resistance
  Application of Ohm's Law
  Voltage Sources in Series
  Kirchhoff's Voltage Law
  Voltage Dividers
  Power in Series Circuits
  Voltage Measurements