## Slide 1: Computer Architecture
Lecture 01
Fasih ur Rehman

## Slide 2: About Instructor
MSc in Electronics and MSc in Systems Engineering in 1994 and 1996 respectively from Quaid-e-Azam University and currently pursuing PhD from CIIT
Worked for Software Industry (developing engineering application) for 5+ years in Pakistan and abroad as well.
Joined CIIT Wah Campus in 2003 as Assistant Professor and worked at various academic and administrative positions since then
Research Interests Mathematical Modeling, Computational Electromagnetics

## Slide 3: Course Contents
Control unit design,
Instruction execution and sequencing of control signals. Hardwired and Micro programmed control.
Input-output – programmed, interrupt driven and DMA I/O and interface design.
Arithmetic logic unit implementation, addition, subtraction, multiplication and division operations for integer and floating point numbers.
Memory organization, memory hierarchy, cache memories – mapping functions and page replacement policies, memory management requirements and virtual memory hardware support.
Fundamentals of computer communication and error control.

## Slide 4: Recommended Book(s)
Computer Organization and Embedded Systems
by
C Hamacher …, 6th Edition 2012
Structured Computer Organization
by
Andrew S Tanenbaum 5th Edition

## Slide 5: Why Computer Architecture
The computer lies at the heart of the computing.
The computer should not be regarded as just a black box that executes program by magic.
All computing students must develop understanding of functional components, their characteristics, their performance and their interactions.
Students need to understand computer architecture in order to
  Structure a program so that it runs more efficiently on a real machine.
  In selecting a system to use, they should to able to understand the tradeoff among various components, such as CPU clock speed, memory size etc.

## Slide 6: Learning Outcome
After successful completion of this course, a student should be able to
  know internal architecture of a processor
  understand how instruction are executed
  know how cache is organized and function
  know memory organization and virtual memory systems
Thus exploiting this hardware to design an efficient software
Describe performance of a computer system based on such parameters
Should be able to design a processor, cache system and virtual memory system

## Slide 7: Von Neumann Architecture
Instructions and data are stored in memory
Memory is region with binary data and every location has a unique address
Instruction can only be executed in a CPU register
Each high level language instruction is translated in many machine instructions

## Slide 8: Fundamental Concepts

## Slide 9: Execution
Execution is based on one of the following operations
  1. Transfer word of data from register to another or the ALU
  2. Perform arithmetic or logical operation and store result in a register
  3. Fetch contents of a memory location to a register
  4. Store register to a memory location

## Slide 10: Memory Unit
Stores Programs and Data
Two catagories
  Primary
    Fast
    Holds program during execution
    Semiconductor cells
    Each location has a unique address
    Processed in words
    Random Access Memory (RAM)
    Access time
    Hierarchy
  Secondary
    Larger
    Cheeper

## Slide 11: Arithmetic and Logic Unit
Computer operations are executed in ALU of the processor.
Load the operands into memory – bring them to the processor – perform operation in ALU – store the result back to memory or retain in the processor.
ALU

## Slide 12: Control Unit
All computer operations are managed by the control unit.
The timing signals that govern the I/O transfers are also generated by the control unit.
Control unit is usually distributed throughout the machine.
How control signals can be generated
  Hard-wired Control
  Micro-programmed Control

## Slide 13: Input and Output
Data processed by the computer is not necessarily in the memory
Data has to be exchanged among peripheral devices and outside world
The way I/O operations are performed have impact on performance of the computer
Input devices keyboard, mouse, graphic tablet etc.
Output devices: Monitor, printer, plotter etc.

## Slide 14: Basic I/O
I/O is the means by which data are transferred between the processor and the outside world
Devices operate at different speeds to the processor so handshaking is required

## Slide 15: Keyboard / Display
The keyboard and display are coordinated via software
Register (on device) assigned to the keyboard hardware
  DATAIN contains ASCII of last typed character
  SIN is the status control flag, normally 0. When a character typed, becomes 1.After the processor reads DATAIN, it is automatically set back to 0
Register (on device) assigned to the display hardware
  DATAOUT receives a character code
  SOUT is the status control flag. It is 1 when ready to receive a character, set to 0 when the character is being transferred
These registers form the respective device interface

## Slide 16: Computer Operations
The computer accepts information in the form of programs and data through an input unit and stores it in the memory.
Information stored in the memory is fetched under program control into an arithmetic and logic unit, where it is processed.
Processed information leaves the computer through an output unit.
All activities in the computer are directed by the control unit.

## Slide 17: Summary
Introduction to the course
Basic functional units of the computer
Basic I/O