## Slide 1: Computer Architecture
Lecture 10
Fasih ur Rehman

## Slide 2: Last Class
Central Processing Unit
  Internal Arch
  Familiarization with the units of CPU
  their functioning
  Memory operations

## Slide 3: Today’s Agenda
CPU Architecture and Operation
Execution of Complete Instruction
Execution of Branch Instruction
Multiple Bus Architecture

## Slide 4: Register Transfer
Input and output of register Ri controlled via switches Riin and Riout
R4 ← R1: Set R1out to 1 and R4in to 1 (others all 0)
All transfers synchronized to a processor clock
Riout called tri-state buffer
B
A
Z
ALU
Y
in
Y
Z
in
Z
out
R
i
in
R
i
R
i
out
b
us
Internal processor
Constant 4
MUX
Figure 7.2. Input and output gating for the registers in Figure 7.1.
Select

## Slide 5: Arithmetic or Logic Operations
The ALU is a combinational circuit that has no internal storage.
ALU gets the two operands from MUX and bus. The result is temporarily stored in register Z.
What is the sequence of operations to add the contents of register R1 to those of R2 and store the result in R3? i. e. R3 ← R1+R2
  R1out, Yin
  R2out, SelectY, Add, Zin
  Zout, R3in

## Slide 6: Fetching Word from Memory
MDR, MAR connections to bus controlled as in figure
For Move (R1),R2
  1. MAR←[R1]
  2. Start read on memory bus
  3. Wait for Memory Function Completed (MFC) from memory
  4. Load MDR from bus
  5. R2←[MDR]
Control Signals
  1. R1out, MARin, Read
  2. MDRinE, WMFC (wait for MFC)
  3. MDRout,R2in

## Slide 7: Storing a Word in Memory
Move R2,(R1) is similar to the previous example
  1. R1out, MARin
  2. R2out, MDRin, Write
  3. MDRoutE, WMFC

## Slide 8: Execution of Complete Instruction
Add (R3), R1
  Fetch the instruction
  Fetch the first operand (the contents of the memory location pointed to by R3)
  Perform the addition
  Load the result into R1

## Slide 9: Execution

## Slide 10: Execution
Increment PC
  Step 1: PC loaded into MAR, read request to memory, MUX selects 4, added to B (PC) and stored in Z
  Step 2: Z moved to PC while waiting for memory
Memory Fetch
  Step 3: Word fetched from memory and loaded into IR
Instruction Decode
  Step 4: figure out what the instruction should do and set control circuitry for steps 4-7. R3 transferred to MAR and memory read operation initiated
Register Transfer
  Step 5: contents of R1 moved to Y

## Slide 11: Execution (Cont.)
Addition
  Step 6: read operation completed and is in MDR as well as B input of ALU. SelectY as second input of ALU and addition performed
Completion
  Step 7: result is transferred to R1, End causes a goto step 1

## Slide 12: Execution of Branch Instruction
Steps 1-3, instruction fetch
Step 4: add the offset to the PC
Step 5: update the PC
Now do you understand why the branch offset is calculated from the next address to be executed?
For conditional e.g. branch < 0, step 4 is replaced with
• Offset-field-of-IRout, Add, Zin, If N=0 then End

## Slide 13: Branch Instruction
Control sequence for unconditional branch instruction
Step
Action
1
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
2
Z
out
PC
in
,
Y
in
,
WMF
C
3
MDR
out
IR
in
4
Offset-field-of-IR
out
,
Add,
Z
in
5
Z
out
,
PC
in
,
End

## Slide 14: Summary
CPU Architecture and Operation
Execution of Complete Instruction
Execution of Branch Instruction
Multiple Bus Architecture