## Slide 1: Computer Architecture
Lecture 22
Fasih ur Rehman

## Slide 2: Last Class
Floating point numbers
IEEE Standard

## Slide 3: Today’s Agenda
Floating Point Numbers
  IEEE Standard for representation of Floating Point Numbers
  Floating point Arithmetic

## Slide 4: IEEE Standard for Representation

## Slide 5: Example

## Slide 6: Special Values
S. No | E’ | M | Value
1 | 0000 0000 (0) | 0 | 0
2 | 0000 0000 (0) | ≠ 0 | De normal value
3 | 1111 1111 (255) | 0 | Infinity
4 | 1111 1111 (255) | ≠ 0 | NaN

## Slide 7: Special Values
Infinity can positive or negative depending upon sign bit
De normal values are used to allow gradual underflow
  Denormal value is smaller than the smallest value that can be represented
NaN means Not a Number: 0/0 or square root of a negative number

## Slide 8: Main Features
Floating point numbers are represented in a normalized form.
MSB of the mantissa is always equal to 1.
We can represent numbers without storing the MSB.
The values of the numbers represented in the IEEE single precision notation are of the form (+,-) 1.M x 2(E - 127)

## Slide 9: Addition / Subtraction Rules
Choose the number with the smaller exponent and shift its mantissa right a number of steps equal to the difference in exponents.
Set the exponent of the result equal to the larger exponent.
Perform addition/subtraction on the mantissas and determine the sign of the result.
Normalize the resulting value, if necessary.
3.1415 x 108 + 1.19 x 106 = 3.1415 x 108 + 0.0119 x 108 = 3.1534 x 108

## Slide 10: Multiplication Rules
Add the exponents and subtract 127 to maintain the excess-127 representation.
Multiply the mantissas and determine the sign of the result.
Normalize the resulting value, if necessary.

## Slide 11: Division Rules
Subtract the exponents and add 127 to maintain the excess-127 representation.
Divide the mantissas and determine the sign of the result.
Normalize the resulting value, if necessary.

## Slide 12: Implementation of Addition

## Slide 13: Summary
Floating Point Numbers
  IEEE Standard for representation of Floating Point Numbers
  Arithmetic