## Slide 1: Computer Architecture
Lecture 27
Fasih ur Rehman

## Slide 2: Last Class
Cache Memories
  Mapping Functions

## Slide 3: Today’s Agenda
Memories
  Performance Considerations
  Virtual memory

## Slide 4: Performance
Performance of a computer depends on
  the speed at which, instruction is fetched in the processor
  speed of the execution of the instruction
  Instructions and Data are quickly accessible when referenced memory locations are present in cache.
  Performance, therefore, depends upon cache miss or cache hit

## Slide 5: Hit Rate and Miss Penalty
The number of hits stated as fraction of all attempted accesses is called Hit Rate
Miss Rate is the number of misses stated as fraction of attempted accesses
The extra time needed to bring the desired information into the cache is called the Miss Penalty

## Slide 6: Hit Rate and Miss Penalty
Goal is to have a memory system with speed of cache and size of a hard disk
High hit rates (> 90%) are essential
  Miss penalty must also be reduced
Example
  h is hit rate
  M is miss penalty
  C is cache access time
  tav Average access time
tav = hC + (1-h)M

## Slide 7: Hit Rate and Miss Penalty
Hit rate can be improved by increasing block size without changing the cache size
  For best results, block size has to be kept of optimal size, neither very large nor very small blocks yield good results
When loading new blocks into cache, if used, load-through approach can reduce miss penalty.
  Load – through approach: In case of a read miss, the requested info may also be sent to the processor as soon as it is transferred to the cache without waiting for the transfer of the whole block.
Write buffers can be used to speed up writing in both write through and write back protocols.

## Slide 8: Contents of Memory Space
For 32-bit memory, every process assumes 4GB of address space available to it.
Memory contents for each process are
  Program’s EXE image
  Any non-system DLL
  Program’s global data
  Program’s stack
  Dynamically allocated memory
  Memory mapped files
  Inter-process shared memory blocks
  Memory local to specific executing thread
  Special memory blocks like virtual memory tables
  OS kernel and DLL’s

## Slide 9: Virtual Memory
Using cache memory, we got improvement in speed of the memory.
Now we’ll discuss an architectural solution that enhances the effective size of the memory of a computer system
This arrangement is called virtual memory.
  Number of address bits in a computer determines the size of the maximum addressable space.
  Generally, computers don’t have that much physical memory
  Programs, these days are huge and don’t fit in MM but are stored in hard disks
    Virtual memory creates illusion of this large memory by bring small pieces of programs to MM from secondary storage device.

## Slide 10: Virtual Memory
Concept of Virtual memory is similar to cache memory
Cache Memory
  Bridges the speed gap between the processor and main memory
  Implemented in hardware
Virtual Memory
  Bridges speed gap between main memory and secondary memory
  Partly implemented in software

## Slide 11: Summary
Performance considerations
Virtual Memory