## Slide 1: Computer Architecture
Lecture 03
Fasih ur Rehman

## Slide 2: Last Class
Bus Organization
Operational Concepts of a Computer
Software (System/Application)
Caching/clock
Performance

## Slide 3: Today’s Agenda
Fetch and Execute
Registers
Memory locations and addresses
Addressing Modes

## Slide 4: Execution
Instruction Fetch
Instruction is decoded
  Register Transfer
Instruction thus is executed
Results are stored

## Slide 5: CPU Registers
Instruction register (IR)
Program counter (PC)
Memory address register (MAR)
Memory data register (MDR)
General-purpose register (R0 – Rn-1)

## Slide 6: Memory Locations
Memory consists of huge number of storage cells, each stores 1 bit.
Data is usually accessed in group of n-bit groups. n is called word length.
second word
first word
Figure 2.5. Memory words.
n
bits
last word
i
th word
•
•
•
•
•
•

## Slide 7: Example of Word

## Slide 8: Memory Addresses
Memory can either be retrieved as one word or one byte (8-bit), addresses, however, for each location are needed.
A k-bit address memory has 2k memory locations 0 – 2k-1, memory space.
24-bit memory: 224 = 16,777,216 = 16M (1M=220)
32-bit memory: 232 = 4G (1G=230)
1K(kilo)=210
1T(tera)=240
Byte locations have addresses 0, 1, 2, … For 32 bit word length, successive words addresses are 0, 4, 8,…

## Slide 9: Word Alignment
  The addresses that begin at byte addresses in multiples of the number bytes in a Word are said to be aligned in memory
  32-bit word: word addresses: 0, 4, 8,….
  64-bit word: word addresses: 0, 8,16,….

## Slide 10: Memory Operation
Load (or Read or Fetch)
  Copy the content. The memory content remains unchanged.
  Address – Load
  Registers can be used
Store (or Write)
  Content of the memory is overwritten
  Address and Data – Store
  Registers can be used

## Slide 11: Primitive Operations
A computer must have instructions capable of performing four types of operations
  Data transfers between the memory and the processor registers
  Arithmetic and logic operations on data
  Program sequencing and control
  I/O transfers

## Slide 12: Register Transfer
Location can be identified by symbolic name (Loc, R0)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
For Example in Assembly language
  Move LOC, R1 = R1←[LOC]
  Add R1, R2, R3 = R3 ←[R1]+[R2]

## Slide 13: Using CPU Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 64 registers need 6 bits)
Potential speedup
Minimize the frequency of memory access

## Slide 14: Branching

## Slide 15: Condition Codes
Condition code flags
Condition code register / status register
  N (negative)
  Z (zero)
  V (overflow)
  C (carry)
Different flags are affected by different instructions

## Slide 16: Addressing Modes
Implied
  “ADD M[AR]” in “One-Address” instruction
Immediate
  Use of a constant in “MOV R1, 6”, i.e. R1 ← 6
Register
  Indicate which register holds the operand
Register Indirect
  Indicate the register that holds the number of the register that holds the operand
    MOV R1, (R2)
Autoincrement / Autodecrement
  Access & update in 1 instr.
Direct Address
  Use the given address to access a memory location

## Slide 17: Addressing Modes
Indirect Address
  Indicate the memory location that holds the address of the memory location that holds the data
Relative Address
  EA = PC + Relative Addr
Indexed
  EA = Index Register + Relative Addr
Base Register
  EA = Base Register + Relative Addr

## Slide 18: Addressing Modes

## Slide 19: Summary
Fetch and Execute
Registers
Memory locations and addresses
Addressing Modes