## Slide 1: Computer Architecture
Lecture 30
Fasih ur Rehman

## Slide 2: Last Class
Computer Communication

## Slide 3: Today’s Agenda
Data Communication
  Multiplexing
  Error Detection and Correction

## Slide 4: Multiplexing
More than one signals using same channel simultaneously for communication.
  Advantage is Cost effective
Types of Multiplexing
  Frequency Division Multiplexing (FDM)
  Time Division Multiplexing (TDM)
  Wavelength Division Multiplexing
  Code Division Multiplexing

## Slide 5: Frequency Division Multiplexing
Non – overlapping frequency ranges are assigned to each user or signal in a medium
  Signals are transmitted simultaneously but use different frequencies
  Oldest multiplexing technique
  Used in analog domain
  more susceptible to noise
  Broadcast Radio and Television, Cable TV, and AMPS cell phone system

## Slide 6: Frequency Division Multiplexing

## Slide 7: Time Division Multiplexing
Available time of the channel is shared by the users
Digital signals used TDM
Two basic types
  Synchronous Time Division Multiplexing
  Statistical TDM
T1/E1and Integrated Services Digital Network (ISDN) use TDM

## Slide 8: Time Division Multiplexing

## Slide 9: Synchronous Time Division Multiplexing
Two sources may generate bits at different rates
Multiplexor inserts sequence of 1s and 0s alternatively for the source that is not generating bits
Very popular
  T-1, ISDN and SONET use this
Bandwidth requirement is same as that of all sources

## Slide 10: Synchronous Time Division Multiplexing

## Slide 11: Statistical Time Division Multiplexing
Time slots are allocated to active nodes only
Make efficient use of bandwidth
  Good for low bandwidth application

## Slide 12: Wavelength Division Multiplexing
Each message is given a different frequency
  Used in Optical fiber

## Slide 13: Code Division Multiplexing
Same frequencies are used at same time but different code is used for different messages
Also called Code Division Multiple Access (CDMA)
Mobile phone systems use this

## Slide 14: Layered Structure
Layered structure is used to reduce the complexity of tasks
A Seven layered model Open System Interconnection is a popular choice.
  Each layer has its own job and protocol

## Slide 15: OSI Model

## Slide 16: Error Detection
Data transfer between two devices must be error free.
Data Can be corrupted during transmission
A reliable communication system must have capability to detect and correct errors.
Error detection and correction is implemented at the data link or transport layer of the ODI model
Types of errors are
  Single bit errors
  Multiple bits errors
  Burst Errors

## Slide 17: Error Detection
Redundancy is used to detect errors
  Vertical redundancy
  Horizontal redundancy
  Cyclic Redundancy

## Slide 18: Error Correction
Two ways possible
  A re-transmit message can be sent to the sender
  Receiver can use error correcting codes.

## Slide 19: Summary
Data Communication
  Multiplexing
  Error Detection and Correction